## Slide 1: Instrument Design

## Slide 2: How to find the optimal geometry of the tool?
Workspace Study
  Normal, high quality MRI scan of the middle ear -> 3D model using lab software
  Analyze/quantify the workspace volume, and what anatomical obstacles are there (include bones, facial nerve, etc.)
Optimize Tool Design
  Start very simple: eg. A straight, rigid instrument, with one curve or one bend
  Analyze how it can move in the model
  Figure out if pitch, yaw, roll is required
  Add more mechanisms based on what is required after this analysis

## Slide 3: How to access recesses in the middle ear?
Controlled tool bending
Pre-shape tools to optimized angles/curvatures calculated using 3D ear models

## Slide 4: Mechanisms
Concentric Tubes
  https://www.youtube.com/watch?v=IUg4Jco-Apc
  Push the curved tube out of a straight tube
  Can have multiple tubes to widen workspace
  Can preshape the curve
Wrist
  Requires cable running along the inside of the tube
  Problem: slits can become blocked
  by tissue
Notes: - Will concentric tubes work in a semi-wet environment? How well would they slide in the ear surgery environment?

## Slide 5: Existing Handle Designs
Requirement: hand/wrist must remain steady during actuation
Fingers gripping the tool must perform the actuation

## Slide 7
Handle can be modified so the fingers are actuating instead of the whole hand